## Slide 1: Progress and Plans for the DIII-D Program
by
D.N. Hill
Presented at the
Fusion Power Associates Annual Symposium
Washington, D.C.
December 13, 2016

## Slide 2: The DIII-D National Fusion Program Advances Fusion Energy Development By Focusing on Four Research Elements
DIII-D Research Elements | Enabled by DIII-D Enhancements
Control Transient Behavior | 
Strengthen the Scientific Basis for Fusion Energy | 
Develop Relevant Boundary Solutions | 
Determine Path to Steady-State | 
Improved 3D control
Increased co-current,
off-axis current drive
Bolometer upgrades
Divertor closure modifications
Improved diagnostics
Helicon
2nd SPI
Tungstencoated rings
Increased electron
Heating/current drive
HFS LHCD?

## Slide 3: DIII-D Goal: Establish the Physics Basis for Avoiding Transient Events Due to Disruptions (Integrated Strategy)
High performance steady-state regimes offer improved stability
Real-time warning of approach to stability limits enables corrective action → Localized current profile control (ECCD) and 3D fields
Ensure disruption mitigation works as last line of defense
ITER-prototype 2nd SPI
Tearing mode amplitude
Response

## Slide 4: Encouraging Results For Disruption Mitigation With Shattered Pellet Injection (Adopted by ITER)
Large cryogenic pellet shattered in guide tube provides pulse of tiny solid shards
Varying deuterium / neon mix provides control of disruption characteristics
Achieved first demonstration of runaway electron plateau dissipation with SPI
Installing 2nd SPI (ITER prototype) to study asymmetries
Increases confidence that SPI will be an effective disruption mitigation tool for ITER

## Slide 5: Gamma Ray Spectroscopy Reveals Growth of High Energy Runaway Electrons (REs) Is Matching Theory
High energy REs grow with electric fields E/Ecrit~2
  Theory predicts growth at E/Ecrit~1.6
  Lower energy RE growth at higher E/Ecrit~5
High energy REs are more difficult to dissipate  better to prevent initial growth
Gamma ray imaging camera

## Slide 6: DIII-D/ASDEX–U RMP-ELM Experiments Represent An Important Milestone for ELM Transient Control
DIII-D experiments identified key elements in AUG compatible shape
  Low n* & triangularity important (enhance plasma response)
AUG established ELM suppression
  Raised d increased performance
Excellent confinement & effective tungsten exhaust
RMP-ELM suppression proven with metal wall
Notes: OVERLAY RMP? CONTEXT SLIDE…

## Slide 7: Significant Fast Ion Transport & Losses Result From Interplay of Energetic Particle Driven Modes
DIII-D: enhanced transport when modes overlap
fTAE
fRSAE-min
Multiple Interacting RSAEs in DIII-D

## Slide 8: Significant Fast Ion Transport & Losses Result From Interplay of Energetic Particle Driven Modes
DIII-D: enhanced transport when modes overlap
ECH changes temperature gradient, removing mode overlap
Simulation now predicts existence and evolution of RSAEs
ECH modification of RSAEs in DIII-D
fRSAE-min
fTAE
fTAE
fRSAE-min

## Slide 9: Significant Fast Ion Transport & Losses Result From Interplay of Energetic Particle Driven Modes
Experiments and simulation are improving predictive capability for ITER
DIII-D: enhanced transport when modes overlap
ECH changes temperature gradient, removing mode overlap
Simulation now predicts existence and evolution of RSAEs
ECH modification of RSAEs in DIII-D
fRSAE-min
fTAE
fTAE
fRSAE-min

## Slide 10: EPED Model Is Providing a Framework for Optimizing the Edge Pedestal to Avoid ELMs and Increase Confinement
Increasing pedestal stability supports higher core plasma performance

## Slide 11: EPED Model Is Providing a Framework for Optimizing the Edge Pedestal to Avoid ELMs and Increase Confinement
Increasing pedestal stability supports higher core plasma performance
QH-mode maintains high pedestal without exceeding ELM threshold
•
0.85
0.90
0.95
1.00
r
Previous high torque QH-mode
Low-torque Wide pedestal QH mode

## Slide 12: EPED Model Is Providing a Framework for Optimizing the Edge Pedestal to Avoid ELMs and Increase Performance
•
0.85
0.90
0.95
1.00
r
Previous high torque QH-mode
Low-torque Wide pedestal QH mode
Increasing pedestal stability supports higher core plasma performance
QH-mode maintains high pedestal without exceeding ELM threshold
Extending Super H-mode may yield further increases in performance

## Slide 13: Theory-Experiment Validation Has Increased Confidence in ITER Achieving its Q=10 mission
Self-consistent coupling of core & pedestal theoretical models
  No free or fit parameters
Whole profile iteration converges to unique solution
  Predicts βN to ~15% in 200 DIII-D cases
Enables prediction and optimization of ITER fusion gain: Q~12 possible
New computing frontier: Multi-scale turbulence simulations
Results reported at IAEA FEC 2016
(TGLF+NEO)

## Slide 14: DIII-D Boundary/PMI Center Is Developing the Scientific Basis for Advanced Divertor Solutions
Research Goals
Use enhanced diagnostics to identify physics and validate models
Vary geometry and configuration: to test predictive capability
Work with materials community to assess candidate materials
Tungsten W182
DiMES
Divertor Closure Experiments
Model Validation: Helium Detachment
Measured
Prad
SOLPS Prad
Divertor Erosion and Migration

## Slide 15: Ion Drifts Produce Strong Divertor Asymmetries in Particle Flux and Detachment Threshold Density
∇B drift into divertor: Asymmetric Te, ne and detachment
Divertor Thomson Scattering Data

## Slide 16: Ion Drifts Produce Strong Divertor Asymmetries in Particle Flux and Detachment Threshold Density
Including drifts in models reproduces major features
∇B drift into divertor: Asymmetric Te, ne and detachment
∇B drift out of divertor: Symmetric Te, ne and detachment
Divertor Thomson Scattering Data

## Slide 17: Obtained First Evidence that Non-Axisymmetric Inter-ELM Heat Flux Is Eliminated During Detachment
Heat flux profile is broadened with RMP, exhibiting a structure indicative of non-axisymmetric striations, also seen in Te profile
3D heat flux striations between ELMs are eliminated at high density
  Before partial detachment and continuing through to detachment
Low density
High density, detached
Heat flux (MW/m2)
2
1
0
2
1
0
1.38
1.42
1.46
1.50
R(m)
Suggests ITER should not see divertor asymmetries from RMP ELM suppression

## Slide 18: AT Operation With Tungsten Divertor Target Achieved Similar Performance As With Carbon (With Caveats)
Best results with on-axis ECH
Accumulation highly sensitive to profiles
Tungsten radiation sensitive to Te profile and time history
  Prad sensitive to Te =3-4keV
  Recombination slower than ionization

## Slide 19: DIII-D Targets Key Priorities in Fusion Development
ITER success
  Operational basis for rapid progress to Q=10
  Resolve (few) remaining design issues
  Scientific basis for confident projection and exploitation of ITER
Path to Fusion Energy
  High b Advanced Tokamak
  Power handling: divertor & materials
Address through focus on underlying physics & exploration

## Slide 20: Profile Flexibility Will Enable DIII-D to Study the Physics of High bN Operation For Attractive Reactor Solutions
Research will explore key profile dependencies in high b regime
  Stability above the no-wall limit
  Turbulence modification by magnetic shear
  Fast ion redistribution physics
Enabled by increased off-axis current drive and electron heating:
  One-year shutdown to add 2nd off-axis beam for current drive
  Increased ECH (1.5MW 117Ghz) for H&CD and mode control
Normalized radius
0
1
On axis beam
Off axis beam
ECCD
J||
Flexible profile tools:
Current Profile
Broad
Peaked
Current Profile
Broad
Peaked
Will determine scientific foundations and existence proofs for viable steady state
Co-cntr
LTO3: 2nd
OANBI

## Slide 21: Actively Investigating Alternative Approaches to Potentially Reactor-Relevant Off-axis Current Drive
High efficiency at high density
Challenge: adequate coupling
Low power test: good loading in high beta AT plasma
Planning for 1 MW test
Helicon Wave Current Drive
High-field Side LHCD (MIT)
Low power test antenna
High efficiency, proven technology
Quiescent inner SOL should allow smaller gaps, good coupling
Evaluating possible launcher locations and waveguide routing, using C-Mod hardware
Notes: with 12-element phased-array antenna at < 0.4 kW (476 MHz)

## Slide 22: EAST Collaboration Provides New Power Supplies to Advance Physics of 3D Fields
ASIPP poloidal field AC power supply increases shaping flexibility and capability for high-current, multi-mode 3D fields
New physics & control includes
  Multiple-n excitation of plasma modes
  Actuator sharing for ELM control, error field correction, MHD spectroscopy, etc.
New Coils will advance physics & control
  Broader n-spectrum: n  6
  Greater selectivity in m-spectrum
  for Torque control, ELM control, …
Further 3D coil sets are being considered
Possible New Coil Sets

## Slide 23
Advanced Divertors Should Minimize and Simplify the Volume Needed for Reliable Dissipation of Plasma Losses
Improve physics understanding to develop improved divertor concepts
  Enhanced measurements to isolate physics
  Systematic divertor modifications to determine key dependencies
  Compare against state-of-the art numerical simulation
Test Advanced Materials for fusion
  Evaluate erosion, migration and re-deposition on a variety of scales
  Assess impact and mitigate impacts on core plasma
Assess compatibility with high performance core
ITER divertor module
Validated models are essential for extrapolating to future devices and to design optimized divertors

## Slide 24: New Divertor Is Being Installed for FY17 Experiments to Increase Operating Window for Divertor Detachment
Phase IA (FY16-17): SAS prototype test
  Reshape the upper divertor tiles to increase divertor closure (SOLPS)
  Essential diagnostics (Langmuir Probes, TC, spectroscopy, DTS)
  Compatible with AT shaping

## Slide 25: New Divertor Is Being Installed for FY17 Experiments to Increase Operating Window for Divertor Detachment
Phase IA (FY16-17): SAS prototype test
  Reshape the upper divertor tiles to increase divertor closure (SOLPS)
  Essential diagnostics (Langmuir Probes, TC, spectroscopy, DTS)
  Compatible with AT shaping
Phase IB (LTO3): Validation of SAS physics basis
  Complete significant diagnostic enhancements
  Improve tile shaping if needed
Phase II (FY19): Improved divertor
  Demonstrate improved detachment with Pumping
  Test compatibility with AT

## Slide 26: New Boundary Diagnostics Target Key Parameters for Boundary Model Validation Studies
Lyman-alpha imaging
New bolometer view chords
New VUV Spectrometer
Detached
160380.3180
Attached
160380.1680
New Divertor Thomson Chords
Divertor Flow Imaging
Rev Btor
Fwd Btor

## Slide 27: DIII-D Expects To Operate 14+3 Weeks in FY17 (Depending on Funding)
Vessel is open now for upper-divertor modifications, diagnostic improvements, and system refurbishments.
Near-term operating schedule (FY17-18) awaits budget and DOE guidance (present guidance is 14 weeks)
Working toward year-long torus opening (LTO3) starting Aug. 2017 to modify a beam-line for Co-counter Off-Axis injection
Now developing plans for two special research campaigns:
  NSTX-U National Campaign (39 proposals for 2 operating weeks)
  Frontier Science Evaluation Campaign (fundamental plasma physics)
    Engage university programs for non-fusion plasma research
    Small working group now evaluating ideas for 1 additional run week.
Now starting preparation of the research plan for FY 2019-2024
  Evaluating research emphases and potential facility upgrades
  Will discuss at a Program Advisory Committee meeting in March 2017

## Slide 28: DIII-D Program Will Continue Working With World Tokamak Programs to Prepare for ITER and Future Next-step Devices
NSTX-U
DIII-D
JET
MAST-U
ITER
ASDEX-U
SST-1
EAST
KSTAR
JT-60SA
TCV
Develop physics basis for controlled high performance scenarios
Extend to long-pulse operation on superconducting devices
Develop and evaluate new materials and boundary solutions
International Collaboration Accelerates Fusion Energy Development